## Slide 1: Compressive spectral anomaly detection
Vishwanath Saragadam , Jian Wang,
Xin Li, Aswin Sankaranarayanan
Notes: Hello everyone. I will be giving a talk on compressive spectral anomaly detection
Hyperspectral images are used for identifying material composition of a scene and one of the applications is anomaly detection.
In this talk, I will be presenting a compressive imager to efficiently and directly detect anomalies, thus reducing the measurement load

## Slide 2: Hyperspectral images
Information as a function of space and wavelength
Wavelength
Space
Data from SpecTIR
400nm
2400nm
Notes: Alright, so let’s look at an ubiquitous modality of imaging, the hyperspectral data
Hyperspectral images capture information as a function of space and wavelength,
What it means is that each pixel in the image captures variations across wavelength

## Slide 3: Applications of spectral data
material classification
object recognition
target/anomaly detection
Data from SpecTIR
Notes: The availability of spectral information at each pixel enables numerous applications, including, but not limited to
  Material classification
  Object recognition
  Target/anomaly detection
Of these methods, Anomaly detection is of interest in this presentation

## Slide 4: Anomaly detection
Spectrum of anomalies significantly different from background
Far fewer than signal dimension
400nm
2400nm
400nm
2400nm
Background
Anomaly
Data from SpecTIR
Notes: An anomaly is defined as anything which seems out of place
In case of hyperspectral images, this means that anomalous pixels have spectrum significantly different from the background
By definition, such anomalous pixels are far fewer than the signal dimension itself.

## Slide 5: Acquisition & detection wasteful
Traditional method
  Acquire the complete hyperspectral image, then detect
  Inefficient as it throws away most of the data
Hyperspectral cameras costly and time consuming
  Limited data bandwidth of ADC
  Splitting of light into wavelengths
256X256X356
266 outliers
Anomalies occupy only 4% of spatial data
Data from SpecTIR
Notes: So if we want to detect anomalies, the natural task is to completely measure the data cube and then detect anomalies
However, this means 99% of the data is thrown away
This matters even more, as hyperspectral cameras are quite costly and need a long time to acquire.
So clearly we need an efficient technique, since we only interested in less than 1% of the data.

## Slide 6: Hyperspectal image signal model
Can be decomposed as low rank and sparse signals
Low rank
Sparse
Background
Anomalies
Data from SpecTIR
Notes: Fortunately, hyperspectral images aren’t too random
In fact, they have a very concise signal model, of a decomposition of low rank and sparse signals
In this case, the low rank contribution comes from background, since only few materials will contribute to background
On the other hand, anomalies are far fewer in number, contributing to the sparse part.

## Slide 7: Anomaly detection & sparse signals
Anomaly detection = sparse signal estimation
  Provided we remove the background
Remove the background
Sparse signal
How do we efficiently separate the two?
Data from SpecTIR
Notes: Immediately, we can see that anomaly detection is a very sparse signal acquisition problem,
Provided the background is removed
My contribution is in the form of a two state imager which does exactly this
By removing background spectra, we show that anomaly detection nicely boils down to a sparse signal sensing problem

## Slide 8: Spatially-coded spectrometer
Camera performs spatial coding
Obtains spectral measurements
400nm
2400nm
Spatial coding – Inner product over space
Spectral measurement
Data from SpecTIR
Notes: Okay so time to talk about what kind of measurement system we have at hand
We have a camera which does spatial coding
Essentially, our camera takes an inner product between a certain pattern and our hyperspectral camera, giving spectral measurements

## Slide 9: A two-stage imager
Stage 1 (Subspace estimation):
  Step 1: Estimating background spectrum
    Need knowledge of the background
    Estimate it from a few samples
Data from SpecTIR
Pick random spatial locations
Measure spectrum
Estimate subspace
400nm
2400nm
400nm
2400nm
Notes: So, if we want to remove the contribution of background, we need to know what the background means
If we randomly sample points in a scene, we will get spectrum that very likely represents most of the background points
So we go ahead and find a subspace for the background spectrum
Cosmetics, text alignment, small letters
No full stops in any sentence

## Slide 10: A two-stage imager
Stage 1 (Subspace estimation):
  Step 1: Estimating background spectrum
    Need knowledge of the background
    Estimate it from a few samples
Stage 2 (Anomaly detection):
  Step 1: Obtain spatially-coded measurements
400nm
2400nm
Data from SpecTIR
Notes: So, if we want to remove the contribution of background, we need to know what the background means
If we randomly sample points in a scene, we will get spectrum that very likely represents most of the background points
So we go ahead and find a subspace for the background spectrum
Cosmetics, text alignment, small letters
No full stops in any sentence

## Slide 11: A two-stage imager
Stage 1 (Subspace estimation):
  Step 1: Estimating background spectrum
    Need knowledge of the background
    Estimate it from a few samples
Stage 2 (Anomaly detection):
  Step 1: Obtain spatially-coded measurements
400nm
2400nm
400nm
2400nm
Data from SpecTIR
Notes: So, if we want to remove the contribution of background, we need to know what the background means
If we randomly sample points in a scene, we will get spectrum that very likely represents most of the background points
So we go ahead and find a subspace for the background spectrum
Cosmetics, text alignment, small letters
No full stops in any sentence

## Slide 12: A two-stage imager
400nm
2400nm
400nm
2400nm
Data from SpecTIR
Stage 1 (Subspace estimation):
  Step 1: Estimating background spectrum
    Need knowledge of the background
    Estimate it from a few samples
Stage 2 (Anomaly detection):
  Step 1: Obtain spatially-coded measurements
  Step 2: Projection
    On to complementary subspace of background
Notes: So, if we want to remove the contribution of background, we need to know what the background means
If we randomly sample points in a scene, we will get spectrum that very likely represents most of the background points
So we go ahead and find a subspace for the background spectrum
Cosmetics, text alignment, small letters
No full stops in any sentence

## Slide 13: A two-stage imager
Stage 1 (Subspace estimation):
  Step 1: Estimating background spectrum
    Need knowledge of the background
    Estimate it from a few samples
Stage 2 (Anomaly detection):
  Step 1: Obtain spatially-coded measurements
  Step 2: Projection
    On to complementary subspace of background
  Step 3: Solve as sparse approximation problem
400nm
2400nm
Data from SpecTIR
Notes: So, if we want to remove the contribution of background, we need to know what the background means
If we randomly sample points in a scene, we will get spectrum that very likely represents most of the background points
So we go ahead and find a subspace for the background spectrum
Cosmetics, text alignment, small letters
No full stops in any sentence

## Slide 14: Advantages
Fewer measurements
  Estimation of subspace of rank r:
  Estimation of anomalies:
Direct estimation of anomalous pixels
  Avoids throwing away of data
  No post-processing
Notes: There is a visible reduction in the number of measurements
For estimating the subspace, we need measurements proportional to the subspace
For estimating K outliers, we need measurements proportional to K
This is far less than dimension of the hyperspectral image.
Make sure your O(K) is correct.

## Slide 15: Simulation experiments
256x256x356 HSI of Deepwater horizon oil spill
200 Detected anomalies with 500 measurements for subspace and 5000 measurements for anomalies
Data from SpecTIR

## Slide 16: Performance metrics
128x128x360 image with 79 added outliers marked in yellow
Fraction of correctly detected outliers with various methods with 60dB added noise
Data from SpecTIR
Notes: Our method also outperforms other compressive sensing techniques which jointly recover a low rank and sparse matrix such as SPaRCS and Robust PCA
Image on the left shows the test image we used for characterizing the performance of various algorithm. We created the image by forcing the image to be low rank and sparse with 483 anomalous pixels

## Slide 17: Prototype
objective lens
DMD
scene
condenser lens
slit
collimator
diffraction grating
focusing lens
line sensor
spectrometer
spatial coding
spectral meas.
Notes: So coming back to what our imager looks like
As I mentioned, we need an optical setup that measure spectral with spatial coding
Very simple solution – have a DMD for spatial coding
And a spectrometer for spectral measurements
We also built our own spectrometer.

## Slide 18: Hardware setup
objective
DMD
focusing lens
pinhole
collimating lens
grating
focusing lens
line sensor

## Slide 19: Experiments
64x64x51 image. Anomalies in red circle
64 measurements for subspace, 250 for anomalies, 10 anomalies detected
Notes: We performed anomaly detection with data obtained by the imager we built
The image on the left shows the scene we used for anomaly detection, which consists of printed text on paper. The gray pixels in the red circle consist of anomalies formed by placing a white LED light behind a diffuser
The image on the right shows 10 anomalies marked in red estimated by obtaining 64 measurements for subspace estimate and 250 spatially multiplexed measurements for estimating the outlier
Again, our algorithm very well estimates the anomalous pixels

## Slide 20: Experiments
Image of scene
Spectral signatures at some representative locations
Notes: We show spectral signatures at three different locations
Notice that the anomalous pixel has a distinct peak in blue wavelength region, which makes it an anomaly in the scene
DMD grating issues, have a backup slide.
Change bright line to a darker shade?
Photon noise from BG will kill the results, what do we do?
Adaptive measurements is the answer.

## Slide 21: Experiments
64x64x51 image. Anomalies in red circle
64 measurements for subspace, 250 for anomalies, 10 anomalies detected
Notes: Our second experiment consisted of a scene printed on paper which is predominantly red.
Four pixels within the white circle were illuminated by a red laser. The red laser is indistinguishable from the background
The image on the right shows 4 anomalies marked in green estimated by obtaining 64 measurements for subspace estimate and 100 spatially multiplexed measurements for estimating the outlier
Again, our algorithm very well estimates the anomalous pixels
Why is it challenging?
  Mention that a RGB camera can’t do a good job, and hence this scene is hard

## Slide 22: Experiments
Image of scene
Spectral signatures at some representative locations
Notes: We show spectral signatures at three different locations
Notice that the anomalous pixel has a strong peak in the red region, corresponding to the narrow band laser light
Get rid of top, bottom edges and add a bright frame to differentiate if from the slide background.

## Slide 23: Conclusion
Stage 1:
Estimate subspace for background
Stage 2:
Obtain spatially multiplexed measurements of scene
Take projection onto complementary subspace and solve as sparse approximation problem
Flowchart of proposed algorithm
Our method outperforms many other detection methods
Notes: In conclusion, we proposed a two stage sensing mechanism to estimate anomalies in hyperspectral images
Simulations and real experiments show the superiority of our algorithm in terms of number of measurements needed and estimation accuracy.
Thank you.

## Slide 24: Thank you

## Slide 25: Extra slides

## Slide 26: Effects of DMD as a grating
DMD configuration
  pitch:
  Blaze angle:
Micro-facets act as diffraction grating
Significant only for Infrared wavelengths
  Energy mostly retained in first order for visible wavelengths
Solving for

## Slide 27: Noise due to background removal
Energy of background much greater than anomalies
  Photon noise of background comparable to anomalies
  May reduce performance
This paper models
Correct model to use

## Slide 28: Noise due to background removal
Comparison of our method without and photon noise and 60 dB measurement noise

## Slide 29: Adaptive extension
Problem with direct sensing
  Photon noise from background overwhelms anomalies
Solution: Don’t detect in background area
  Step 1: Estimate background as before
  Step 2: Take a few spatiall-coded measurements to get an approximate area of background pixels
  Step 3: Sense anomalies in non-background pixels
Planned for future work

## Slide 30: Performance metrics
Receiver operating characteristic on a 128x128x360 image with 71 artificially added anomalous spectra.
Notes: Finally, our algorithm outperforms the Reed Xiaoli detector in detecting anomalies
We artificially inserted 71 anomalous targets in a hyperspectral image and performed anomaly detection with our proposed algorithm and
The Receiver operating characteristic curve plots true positives vs false positive
From the plot, it is evident that our method has a larger area under the curve than the RX detector

## Slide 31: Reed-Xiaoli detector
Constant False Alarm Rate detector
Gaussian Log-likelihood Ratio Test
  Background assumed to follow Gaussian distribution
  Anomalies have low likelihood
  Vanilla version a local anomaly detecto
Local patch of hyperspectral image.
Covariance computed over this area
Mean computed over this red area
Guard area. No outliers assumed in this yellow area
Point under test to classify as anomaly